## Slide 1: University of Bridgeport CS/CpE 460 Introduction to Robotics Fall 2011 Project 2: Surveyor SRV-1 Blackfin Lane Detection. Submitted To: Dr. Tarek Sobh Prepared by: Tariq Alshugran Qassim Bani Hani Tamir Yousef

## Slide 2: Introduction
The objective of this project is to utilize the SRV-1 robot camera to detect a lane and then move the robot along the lane. The images will be received from a the robot and then processed on a computer using a third party software then issue the robot a command to move along the lane. To do this, first we need to connect the robot to a computer utilizing the matchport WiFi of the robot, and then the image will be processed using RoboRealm software which will also issue the movement command.

## Slide 3: Connecting SRV-1 to the computer using wireless WiFi
Turn on the SRV-1 robot so that the Matchport is powered. Start your wireless network manager program, and connect to the SRV1 adhoc network.
Ping the robot IP address, in our case the IP address is 169.254.0.10. If the ping was successful and the data was received without any loss then the connection is successful.

## Slide 4: Using RoboRealm Software with SRV-1
In RoboRealm software there are two modules that can connect to SRV-1: SRV1 and SRV1b. The SRV-1 is to connect using COM port, while the SRV1b is used to connect using the WiFi. To start working with the SRV and RoboRealm follow these steps:
  Ensure that you computer is connected to the SRV-1 using wireless network as described previously.
  Download and install the RoboRealm software from http://www.roborealm.com/registration/index.php and then run RoboRealm.exe
  Insert in the SRV1b module.
  Once the module is inserted, edit the module properties to match the robot settings

## Slide 5: Preparing the lanes
In this case we are looking for yellow squares that define a lane for the robot to follow. The lane of squares is created using yellow pieces of thick paper cut into small pieces and placed approximately 6 inches apart. Care needs to be taken to place each square far enough from the previous square otherwise the robot will not be able to see the next square as it loses track of the previous one. The problem is that the robot camera is horizontal with the floor so it can’t detect the ground fully. Once the robot determines that no additional squares are present it will turn around and proceed back over the course.

## Slide 6: Preparing the lanes – Conitue
From the robot's point of view the setup looks quite different than from an overhead view. This is largely due to the proximity of the camera to the ground and the lack of adequate lighting to provide enough contrast in the image. The bad lighting of the setup was done on purpose in order to review image processing techniques that can help in these kinds of environments.

## Slide 7: The Lane Detection Process
After loading the SRV1b module, you should be able now to see the video feed from the robot to the software.

## Slide 8: The Lane Detection Process
Now we have a problem that the camera is horizontal with the floor, so it will not be able to see the lane on the board, to unwrap the frontal view of robot add the perspective module and tilt the image to show only the frontal view with a degree of 0.0099999998.

## Slide 9: The Lane Detection Process
Then add flood filters to show the lane trail:

## Slide 10: The Lane Detection Process
Then crop the image to show only the immediate area immediately in front of the robot by adding crop module and set the values to (0, 0) – (320, 100)

## Slide 11: The Lane Detection Process
Then add a BLOB filter to filter the exact location of the trail and remove background.

## Slide 12: The Lane Detection Process
Now add the center of gravity module to find the center of the blob.

## Slide 13: The Lane Detection Process
Finally add the code to control the motor motion. The code is written in VBScript language and saved in the VBScript module. The point we want the robot to move towards is contained in the COG_X and COG_Y variables. These variables are created by the Center of Gravity module.
To control the motors of the SRV-1b to move towards that point we need to just use the X coordinate and steer left if the point is to the left of the screen or right if the point is towards the right of the screen. Basically we want to control the robot to keep the X COG in the middle of the screen. This will then cause the robot to move along the defined trail and also attempts to keep as much of the significant part of the image (i.e. the squares) in view.
We use the VBScript module to create two motor variables that are then fed to the Surveyor SRV-1b module.

## Slide 14: References
http://www.surveyor.com/cgi-bin/yabb2/YaBB.pl?num=1257565328
http://www.surveyor.com/cgi-bin/yabb2/YaBB.pl?num=1200515001
http://www.surveyor.com/blackfin/SRV_setup_bf.html
http://www.robotreviews.com/reviews/surveyor-srv-1-blackfin-robot-review
http://www.pololu.com/docs/0J7
http://www.surveyor.com/srvdownload/termv19b.zip
http://www.surveyor.com/cgi-bin/yabb2/YaBB.pl?num=1196352263
http://www.voxatec.com/downloads/RoboBrain_Manual.pdf
http://www.roborealm.com/help/Surveyor_SRV1b.php